## Slide 1: Multi-Disciplinary Mechanical Modeling, Management and Exchange
Clark Briggs
ATA Engineering
Clark.Briggs@ata-e.com
(909) 626-6364
1/17/2012

## Slide 2: Content Structure
Model standards for exchange
  AP209, HDF5, CGNS, Nastran deck, …
Management
  Model and data management
  Process management
  Collaborative environments
Multidisciplinary Integration
  Separable, serial, bucket brigade
  Optimization frameworks
  CoSimulation, timestep-by-timestep integration
  Solution process knowledge is in the executables

## Slide 3: Discipline Scope Addressed
Mechanical Analysis
Performance Estimation
Stress, dynamics, heat transfer,
Coupled with
  Fluids for heat transfer, loads, deformed shape
  Control systems
  Propulsion, RF/optics, ECAD thermal
But not…
  Design CAD, electrical/avionics, software, magnetics
Why? Author’s limited experience & limited time to prepare. Nothing fundamental behind the limitations and exclusions.

## Slide 4: Model Exchange Standards
Descriptive models

## Slide 5: STEP AP-209
STEP AP-209 is one of the Application Protocols
Modular AP Domains
  AP203 Mechanical CAD (parts & assemblies)
  AP209 CAE (FEA and CFD)
  AP210 EDA/MCAD (electrical and mechanical assemblies)
  AP233 Systems Engineering
  AP239 Product Life Cycle Support (PLCS)
Source: Charlie Stirk, PDES Inc., “STEP Implementation”, NIST_STEP_TDP2010.pdf
And http://www2.pdteurope.com/media/54176/5. step in the usa – an update from pdes inc.pdf, 2010

## Slide 6: CAx Implementer Forum
www.cax-if.org
Bi-annual rounds of testing of CAD data exchange
  Cooperate on implementing STEP
  Accelerate translator development
  Promote interoperability
  Scope is AP203 and AP214
Joint testing effort of PDES Inc. & ProSTEP iViP with software industry participants
Current test cases includes Composites
  Used with AP209ed2 for CAE
Source: Charlie Stirk, PDES Inc., “STEP Implementation”, NIST_STEP_TDP2010.pdf

## Slide 7: High Level AP209ed2 Composition
Source: http://cms3.dynaweb.nl/users/esa//docs/10C08_SECESA_2010/jotne---secesa-simdm.pdf

## Slide 8: AP209ed2 Multidisciplinary Analysis and Design
Combines CAD, CAE, PDM capabilities
  Superset of AP203ed2
  Finite Element Analysis (FEA)
  Computational Fluid Dynamics (CFD)
  General numerical analysis
  Shares base analysis models with AP233 Systems Engineering
Developing binary API
  Based on open source HDF5 toolkit
Simulation Data Management (SimDM) project
  Analysis data management
  Repository for archiving
  Interfaces to commercial and proprietary simulation tools
  Joint LM Aero and Jotne/EPM Technologies project
Source: Charlie Stirk, PDES Inc., “STEP Implementation”, NIST_STEP_TDP2010.pdf

## Slide 9: Analyses in AP-209
Finite Element Model, 2-D or 3-D
Node representation
  Unique ID with point representation
  May be in a node set
  May be related to design geometry
Element representation
  Unique ID with list of node representations
  May have geometric aspects eg face, edge, or volume
  Has element coordinate system
  Has property representations
AP 209ed1 supports linear static and linear dynamic analyses
  Case and step controls
  Constraints for single nodes, groups, and linear constraint equations
Analysis results
  States for: known a priori, calculated result, linearly superimposed, output request
  Result information represented by 2-D and 3-D field variables
  Information such as notes, warnings or errors represented by messages
  May be related analysis reports represented as documents
Source: “Recommended Practices AP209,” v1a, PDES, Inc., 1999
http://www.steptools.com/support/stdev_docs/express/ap209/recprac209v1a.pdf

## Slide 10
Source: “Recent Developments in STEP”, Charlie Stirk, Collaboration & Interoperability Conference, 17-20 May, 2009, http://www.3dcic.com/2009-proceedings-audio/recent-developments-in-step

## Slide 11: AP-209 ed 2
Renamed Multidisciplinary Analysis and Design
Incorporates CFD based on CGNS
Generalized structured and unstructured analysis and mesh capabilities developed in EU
Complete discrete/continuous mathematical field representation capability based upon the David Talyor Labs/Boeing DT-NURBS package

## Slide 12: AP-209 Status
AP-209 approved 1994
AP-209ed2 approved 2010
CAx-IF (with NAFEMS) testing circa 2002
LM Aero and Jotne/EPM Technologies of Norway are developing an open, standards-based (using AP209 ed2) Simulation Data Manager named SimDM.

## Slide 13: CFD General Notation System (CGNS)
General, portable, and extensible standard for the storage and retrieval of CFD analysis data
Collection of conventions, and free and open software
Designed to facilitate the exchange of data between sites and applications, and to help stabilize the archiving of aerodynamic data
Platform independent API for implementation in C, C++, Fortran and Fortran90
Principal target is compressible viscous flow (i.e., the Navier-Stokes equations), and subclasses such as Euler and potential flows
HDF5 is the default (official) data storage mechanism to enable parallel I/O
Source: “What is CGNS?,” http://cgns.sourceforge.net/WhatIsCGNS.html

## Slide 14: NASTRAN Data Deck
De facto standard for structural FEA model transfer
Bulk data deck is declarative definition
  Node ID, location, degrees of freedoms
  Element ID, nodes, property ID
  Loads and boundary conditions
Case control deck is process parameter definition
  Organization of loads, sequences, parameters
Good commonality still remains
  Divergence between MSC and SPLM since 2004 divestiture
  Exchange participants do need content agreement

## Slide 15: HDF5
Data model, library, and file format for storing and managing data
Flexible and efficient I/O
For high volume and complex data
Completely portable file format
High-level API with C, C++, Fortran 90, and Java interfaces
Range of computational platforms, from laptops to massively parallel systems
Commercial software supporting HDF5
  Matlab, EnSight, ParaView, …
Source: “HDF Group – HDF5, What is HDF5?,” http://www.hdfgroup.org/HDF5/whatishdf5.html

## Slide 16: Simulation Data Management

## Slide 17: Overview
Data Management Scope
  Analysis data sets, files, reports
  Source data (design geometry, material defs, …)
  Results data files, viewables, summaries
  Process, execution, orchestration, tool integration
Application Scope
  Geographical: Departmental, single site, enterprise, global
  Business: Internal projects, OEM-Tier 1 Suppliers, collaborators
  Duration: Work in Process, Release, Archive, Long Term Archival
Life Cycle Phases follow Product
  Proposal, Concept
  Design, Test
  Operations, Maintenance

## Slide 18: Commercial Offerings
ANSYS – Engineering Knowledge Management
Dassault – Simulia Simulation Lifecycle Management
MSC.Software – SimExpert/SimManager
Siemens PLM – Teamcenter for Simulation
Altair – Altair Data Management
Source: “Simulation Data & Process Management – Vendor Scorecard,” Collaborative Product Development Associates/CIM Data, Dec 2009.

## Slide 19: STEP AP237 Product Life Cycle Support (PLCS)
ISO 10303-239-CD edition 2 2009
An international standard
Rich information model
  Activities, plans, schedules, design data, …
Covers product life cycle
A standards based exchange model
Deployment modes
  Point to point translators
  Collaboration hub
Source: “What is PLCS -STEP AP239?,” Bodington and Houbaux, PDT Europe, 11/16/2009 http://www2.pdteurope.com/media/54152/1a. what is plcs - step ap239.pdf

## Slide 20: Example: PLCS Information Model
Source: “What is PLCS -STEP AP239?,” Bodington and Houbaux, PDT Europe, 11/16/2009 http://www2.pdteurope.com/media/54152/1a. what is plcs - step ap239.pdf

## Slide 21: Model Management Challenges
Common w/ Enterprise Data Management
  Security, access control, integrity
  Fragmented data management systems
  Globally dispersed organization w/ business partners
Modeling Related
  Wide variety of file types with little standardization
  Large file sizes (> 1Gb solution files)
  Few standardized processes, e.g. change control

## Slide 22: Multidisciplinary Integration

## Slide 23: Serial Integration aka “Bucket Brigade”
Applicable to coupled but separable physics
  Product of first analysis is input to second analysis
Examples
  Precision structure borne optical systems
  Thermally driven structure fatigue life prediction
  Quasi static analysis where one domain is quite fast relative to the other.
Implementation approach
  Use stand alone solver for first domain
  Transfer output solution to input for second solver

## Slide 24: Loosely Coupled
Cyclically coupled where the output of one solution drives the input to the other, but that response affects the first domain.
  Not separable and serially solvable
Amenable to iterative, cyclic solution
  Assume an input and run the sequence to compute an updated starting point
  Requires strong/good enough convergence
Examples
  Deformed aircraft wing shape under static aerodynamic loads

## Slide 25: Optimization Frameworks
Framework for integration of a wide variety of existing analysis tools
Commonly applied to optimization of performance
Captures and automates an analysis process
Seeks to leverage existing tools as black boxes
  Executed via invocation commands
  Manipulate parameters exposed in input decks and commands
Commercial products
  ModelCenter, Phoenix Integration, http://www.phoenix-int.com/software/phx_modelcenter_10.php
  SIMULIA Execution Engine (formerly Engineous Fiper), http://www.simulia.com/products/see.html
  Workspace, Comet Solutions, http://cometsolutions.com/products/workspace/

## Slide 26: Example: Phoenix Integration ModelCenter
Source: “An Approach to Multidisciplinary Design, Analysis & Optimization For Rapid Conceptual Design,” A. Carty, Paper AIAA-2002-5438, http://www.phoenix-int.com/documents/pubDownload.php/MDOforRCD.pdf

## Slide 27: Example: Comet Workspace
Source: Comet Solutions, http://cometsolutions.com/products/workspace/

## Slide 28: CoSimulation
For inseparable domains that require time synchronous solution
Each solver can run independently for a few (but different) steps, but meet regularly to synchronize
Requires transfer of variables/response between domains at synchronization points
May require iteration for equilibrium at synchronization points

## Slide 29: CoSimulation Frameworks
Technology components (typical)
  User interface
  Executing sequence controller
  Field mapper (surface, volumes, discrete data)
  Client programs (solvers)
  Libraries for communication, control, object creation, and data interpolation
  API layer with language bindings eg Fortran 77, Fortran 90, C, and C+
Examples
  Mesh-based parallel Code Coupling Interface (MpCCI)
  SIMULIA Co-Simulation Engine (CSE)
  Multi-Disciplinary Computing Environment (MDICE)
CSE Source: Blades, E.L., Miskovish, R.S., Luke, E.A., Collins, E.M., and Kurkchubashe, A.G., “A Multiphysics Simulation Capability using the SIMULIA Co-Simulation Engine,” Paper AIAA 2011-3397, 20th AIAA Computational Fluid Dynamics Conference, 27 - 30 June 2011, Honolulu, Hawaii
MDICE Source: Sheta, E.F., Siegel, J.M., Golos, F.N., and Harrand, V.J., “Twin-Tail Buffet Simulation Using a Multi-Disciplinary Computing Environment (MDICE),” CEAS/AIAA/ICASE/NASA Langley International Forum on Aeroelasticity and Structural Dynamics, Williamsburg, Virginia, USA, June 22-25, 1999
MpCCI Source: “MpCCI 4.0.1-4 Documentation,” Fraunhofer SCAI, http://www.mpcci.de/fileadmin/mpcci/download/MpCCI-4.0.1/doc/pdf/MpCCIdoc.pdf

## Slide 30: Solution Process is the Key
For realistic complex problems (beyond serially separable and optimization), process knowledge is embedded in the solver executable.
  Model data definition is not sufficient.
  Case control, execution parameters are not sufficient.
For example, successful CFD requires complex numerical processes that are sensitive to the implementation expression.
As a result, co-simulation is required for the current multidisciplinary analyses of interest.

## Slide 31: Workshop Organizer's Questions

## Slide 32: What is your modeling approach?
For team building a single discipline model
  Common COTS file formats or neutral file format
  Detailed interface negotiation and documentation
  Manual configuration control
For loosely coupled optimization or multi-disciplinary
  Design models w/ solver to expose needed inputs and produce desired outputs
  Provide a compact launchable executable
  Manual configuration control, distill iterations into summary deliverable
For tightly coupled multi-disciplinary
  Custom integrate to a co-simulation framework

## Slide 33: How do you support the integrated modeling vision?
Rich legacy of serial or optimization style integrated examples
Steady progress in standards (AP209ed2) definition
Newly evolving co-simulation frameworks with generalized interface physics and variety of software process techniques
Growing adoption of simulation data management and codified processes

## Slide 34: What are your integration challenges?
Wide variety of phenomena leads to complex physics and complex solver issues
Missing STEP AP209 translators from COTS vendors
Like systems engineering, multi-disciplinary modeling must cross organization boundaries to change existing practices with poorly documented business benefits
Data management is required infrastructure but suffers its own adoption challenges

## Slide 35: How can MBSE help to address the challenges?
Continue formalizing modeling structure
Include STEP AP209 in STEP suite list
Lower cost of STEP implementations
Drive the business case
Pull disciplines into SE-led modeling in projects
Establish cross-society working groups