## Slide 1: (MBSE)2 : Using MBSE to Architect the MBSE System
Ryan Noguchi
The Aerospace Corporation
ryan.a.noguchi@aero.org
January 2020
Approved for public release. OTR 2019-01189.

## Slide 2: The MBSE System
Treat MBSE as a System to be developed with disciplined SE
Implementing MBSE involves integration of many interdependent pieces
  Descriptive models
  Analytical models
  Design models
  Databases
  PLM/ALM tools, RM tools, etc.
These pieces should not be developed in isolation
They should be architected into a coherent MBSE System
  As with any non-trivial system, use systems engineering to architect and implement it
… perhaps even using MBSE

## Slide 3: Comparing the MBSE System to the Real System
Structure and Requirements
 | The Real System
Functional Requirements | What must it do?
Performance Requirements | How well must it do it?
Structure | What system components comprise it? How are those components connected?
Requirement Traceability | Requirements trace to higher requirements
Requirement Allocation | Requirements are allocated to sets of system components
Requirement Verification | Test events verify requirements Test events require components, facilities, test equipment, etc.
The MBSE System
What questions must it answer?
How well must it answer them?
What model components comprise it? How are those components connected?
Questions trace to higher questions and to the decisions they should inform
Questions are answered by sets of model components
Model views answer questions for humans Model views require model components, tool infrastructure, etc.
The MBSE System is itself a System
… amenable to Systems Engineering
… and perhaps also MBSE

## Slide 4: The MBSE System and the (MBSE)2 System
MBSE for the Real System is implemented in an MBSE System
Real System
MBSE System
for the Real System
Model of the
Real System
MBSE System
for the MBSE System for the Real System
Model of the
MBSE System
for the Real System
MBSE System
(MBSE)2 System
MBSE for this MBSE System is implemented in an (MBSE)2 System

## Slide 5: Why Model the MBSE System?
MBSE can add value to the implementation of MBSE
The modeling process can improve discipline in executing the architecting process
The model of the MBSE System can help with managing the complex network of dependencies within the model of the Real System
Components of the (MBSE)2 System can be linked to their counterparts in the MBSE System in the same modeling environment
The experience of modeling the MBSE System can arm acquisition offices with valuable experience in modeling processes, methods, and tools in advance of the formal acquisition
  And aid in the creation of model-based requirements to support that acquisition

## Slide 6: System Architecting Process
Architecting is a nonlinear process intended to illuminate tradeoffs to better inform decisions
Purpose Analysis
Decision Support
Problem Space
Exploration & Refinement
Solution Space
Exploration & Refinement
Harmonization & Analysis
Aerospace System Architecting Method (ASAM)

## Slide 7: Architecting the MBSE System
Purpose Analysis
(MBSE)2 models the Purposes of the MBSE System to connect the modeling effort to its value to stakeholders
Define high-level Objectives for the MBSE System
  i.e., What are the reasons for implementing MBSE?
    Improve development of the Real System?
    Improve operation of the Real System?
    Advance the practice of MBSE?
Identify key Actors for the MBSE System
  Includes all stakeholders for the Real System
  For each Actor, identify their key Concerns
Each part of the MBSE System should be traceable to important Objectives, Concerns, and Actors

## Slide 8: Architecting the MBSE System
Problem Space Exploration & Refinement
(MBSE)2 models the Problem Space of the MBSE System to define the Questions the models need to answer
Identify key Decisions about the Real System
  Key program milestones
  Key programmatic decisions
  Key operational decisions
For each Decision and each Concern, identify the Questions that need to be answered
  Questions may be chained into (or derived from) process workflows
Every part of the MBSE System should be traceable to (answer) one or more Questions
Problem Framing Workshops* found to be effective for fleshing out the problem space
* See James Martin, Problem Framing - Identifying the Right Models for the Job, INCOSE International Symposium, Orlando, FL, 2019

## Slide 9: Architecting the MBSE System
Solution Space Exploration & Refinement
(MBSE)2 models the Solution Space of the MBSE System to identify model components that are needed
Identify the complete Feature Sets of Model Components needed to answer each Question
  Model elements, relationships, attributes, metadata
Create a Conceptual Model of the Model Components
  Documents how they should be used together
Identify useful subsets of the total Scope of Model Components
  Answer Questions incrementally by incrementally implementing scope
    Subset of elements or relationships
    Depth of dependency chain

## Slide 10: Architecting the MBSE System
Harmonization and Analysis
(MBSE)2 models the Harmonization of the MBSE System to define “work packages” needed to answer Questions
Identify the View that answers each Question
  Identify Model Components needed
  If more than one View is needed to answer a Question, the Question may be at too high a level
Identify needed Model View Construction Components to create views
  Query language constructs
  Report templates
  Metachain or constraint expressions
  Automation scripts
Model Components and Model View Construction Components comprise the Feature Sets needed to complete a View

## Slide 11: Implementing the MBSE System
Decision Support
Use agile development methods to implement the MBSE System to provide rapid learning and feedback
Decide what to Build and Plan the Modeling Effort using Agile development principles
  Develop an Initial List of Questions, Views, Components, etc.
  Choose and prioritize Questions to be answered
  Prioritize Feature Sets to be built to answer the Questions
  Decide scope of each sprint—answer one or more Questions per sprint
(Backlog)
(User Stories)
(Features)
(Sprint planning)

## Slide 12: Managing the Implementation of the MBSE System
The (MBSE)2 System as a Development Dashboard
Use the (MBSE)2 model to inform and manage the model development process
Execute the plan using Agile development principles
  Monitor progress using the (MBSE)2 System
    Impact analysis, coverage/gap analysis
  Measure progress by Questions answered
    Quantity
    Quality (scope, depth, fidelity)
  Solicit feedback from Question owners
  Adjust (MBSE)2 model based on feedback and learning
    Update backlog and modeling plan based on evolving knowledge

## Slide 13: Staggered Streams Enables Agile Development
Staggered application of ASAM facilitates agile development of the MBSE System with continuous evolution
Time
Stream starts do not need to be synchronous
All streams continue through life of MBSE System
Use Pathfinders to bootstrap the effort and avoid “analysis paralysis”
Views
Decisions, Questions
Model Components: Elements, Relations, etc.
Model Views, Model View Construction Components
Modeling Plan
Modeling Execution (and Monitoring)
Model Operation (and Feedback)
Problem Space
Solution Space
Harmonization
Decision
Modeling Pathfinder
Modeling Pathfinder Feedback
Objectives, Stakeholders, Concerns
Purpose Analysis

## Slide 14: Operating the (MBSE)2 System
Example Use Case: Model Based Systems Engineering Reviews
Static artifacts go “stale” quickly,
Static artifacts are easily misinterpreted
Static artifacts grow in inconsistency
Models are the life-blood of knowledge management—always current
Models are rigorously defined with far less ambiguity
Models have automated enforcement of internal consistency
Source Material (Requirements, Architecture, CONOPS, Test Plans, etc.)
  Review Events (e.g., SRR, SDR, PDR, CDR, etc.)
Discrete events separated by many months
Discrete large data drops
Changes implemented offline; delta events
Success criteria inconsistently interpreted
Continuous, proactive assessment, minimizing time to discover defects
Comprehensive assessment of linked data across the enterprise
Changes implemented immediately, enabling quicker impact assessment
Success criteria are consistently applied and proactively drive knowledge/model creation

## Slide 15: Operating the (MBSE)2 System
Example Use Case: Model Based Systems Engineering Reviews
Objectives
  Define knowledge to be assessed for maturity at each milestone
    Provide to contractors as “requirements” for model creation and delivery
  Facilitate orderly review of knowledge against success criteria
  Adapt quickly to evolving knowledge
    Use modeling tools to perform impact and coverage analysis
Actors (Stakeholders and Beneficiaries)
  Program Manager
  Program Systems Engineer
  Enterprise Systems Engineer
  Program Review Owner
  MBSE System Modelmaster(s)
  Subject matter experts (SMEs)
Concerns
  All questions (review success criteria) answered?
  Risks identified, quantified, and adjudicated?
  Implications to enterprise identified (and acceptable)?
Decisions
  Has the milestone been successfully achieved?
  Are tradeoffs identified and understood?

## Slide 16: Operating the (MBSE)2 System
Example Use Case: Model Based Systems Engineering Reviews
Questions
  Define success criteria for the review
    Refine criteria until clear how to verify satisfaction
Ref: ISO 15288.2 Standard
Model Components
  Define needed model content to answer each question

## Slide 17: Operating the (MBSE)2 System
Example Use Case: Model Based Systems Engineering Reviews
Assign Questions to reviewers
Determine Views reviewers need to review
Link Real System model to MBSE System model
Assess and track Review completeness
  Coverage analysis, impact analysis, etc.
  As the Real System model evolves, (MBSE)2 model reveals potential impacts to the MBSE System to trigger reassessments

## Slide 18: Key Takeaways
Use MBSE to architect and implement MBSE
Implementing MBSE is really implementing an MBSE System
Apply system architecting methods to architect the MBSE System
Use an agile process to architect, implement the MBSE System
  Staggered parallel processes facilitate continuous progress, feedback, and evolution
An (MBSE)2 System model can facilitate management of complexity & traceability
  Link the MBSE System with the (MBSE)2 System
  Use the (MBSE)2 System to manage the implementation of the MBSE System
  Use the (MBSE)2 System to operate the MBSE System