## Slide 1: Common SysML Conceptual Stumbling Blocks
San Diego INCOSE Mini-Conference 2013.11.02
INCOSE MBSE Workshop 2014.01.27
Rick Steiner
rick@ricksteiner.net
Portions Copyright 2013, Raytheon; Copyright 2014, Rick Steiner/Skygazer Consulting. Unpublished Work.
Portions of this work are from the book Practical Guide to the Systems Modeling Language (SysML), by Sanford Friedenthal, Alan Moore, and Rick Steiner, published by Morgan Kaufmann Publishers, Copyright 2008, 2012 Elsevier Inc. All rights reserved.
Notes: Presentation Title
January 26, 2014
Speaker Name
1

## Slide 2: What do Systems Engineers have problems with when learning SysML?
SysML is too complex! (flexibility vs. complexity)
What does that darn diagram header mean? (models vs. diagrams)
Why do I need both ibds and bdds? (definition vs. use)
  Activity diagrams have no activities on them!* (activity modeling vs. functional hierarchy)
Why not use packages for my product breakdown structure? (composition vs. containment)
How is SysML different than Matlab? (parametric modeling)
Why do I care about Units? (values, value types, units and quantity kinds/dimensions)
Why isn’t SysML executable? (functionality vs. model execution)

## Slide 3: Issue #1: SysML is too complex!
“Traditional” SE can be done with only 3 Basic Diagram Types
Containment,
Composition,
Taxonomy
(definition)
Arrangement &
Connection
(use)
Functional Flow
What do you need?

## Slide 4: Motivation for the Systems Modeling Language
Systems Engineers needed a standard graphical modeling language
  Many different modeling techniques/languages have been used for developing system models:
    Behavior diagrams, IDEF0, N2 charts, Hatley-Pirbhai
    Tools tended to support only one of these techniques/languages
  The SE discipline has lacked a broad-based standard that to support general purpose system modeling needs
Why use the Unified Modeling Language (UML) as a basis?
  UML has become a de facto standard within software engineering
  UML tools and training are widely available, and generally adaptable
  OMG standardization process supports UML customization for specific domains (e.g., systems engineering, real-time, SOA, etc.)
SysML was developed to meet broad SE application
  SE Domain Special Interest Group jointly sponsored by INCOSE and OMG in 2001
  UML Profile for SE followed structured process: RFI , SE conceptual model (2002), requirements analysis, RFP (2003) with clear, detailed requirements for any language supporting systems engineering.
    Submissions needed to demonstrate their compliance with those requirements.
    A panel of INCOSE experts evaluated this compliance before adopting SysML 1.0 in 2006.
  Adoption of SysML by industry indicates that it has met the objective of being a broadly useful system modeling language.

## Slide 5: Issue #2: Those darned Diagram Headers! (Models vs. Diagrams)
Powerpoint & Visio teach us to take diagrams at face value
  They can be manipulated independently, easily abstracted
  I can add whatever I want, without rigor or process
Good modeling tools tend to reinforce this impression
  Drag and drop symbols, easy relationships
But good modelers work mostly from the model browser
  Drag elements from the browser on to the diagram
  Can actually build models without using a diagram at all!
  Tools render/update diagrams from the model
Remember that reports, scripts and checkers run on the Model, not the Diagrams!
Tables and matrices are also excellent model viewers
Good modeling practices are consistent with good diagrams
  Minimize number of elements at each layer of abstraction
  Elide unnecessary information on the diagram… use views/viewpoints
  Give the diagram a meaningful name!

## Slide 6: SysML Diagrams exist in Model Context
Each SysML diagram represents a model element
  This provides the necessary context for every diagram
Each SysML Diagram must have a Diagram Frame
Diagram context (the element it represents) is indicated in the header:
  Diagram kind (act, bdd, ibd, seq, etc.)
  Model element type* (activity, block, interaction, etc.)
  Model element name
  Descriptive diagram name*
*Some parts of the diagram header can be elided, if it doesn’t cause confusion

## Slide 7: Issue #3: Definition and Use in SysML
This is the biggest “stumbling block” for new SysML users without a software background
  “Why do I need BOTH a bdd and an ibd?”
  If you need to ask the question, just build the ibd!
    bdd’s are NOT mandatory, but you will eventually want them.
    Building the bdd later will cause minor rework.
    bdd’s and ibd’s are complimentary aspects of a single structural model
  Same principle applies to parametric & activity models
Definition vs. Use:
  Define a model element in one place in the model.
  Use it everywhere it is needed. Don’t redefine it unless you need to.
See the “structure” corner of the pillars chart
Mechanical engineers have less problem with this
  They are used to defining parts, then using them

## Slide 8: Example of Definition vs. Use
definition
use

## Slide 9: Issue #3a: Activity Modeling & Functional Hierarchy
Activity models are intuitive
  Functional flow, control & data flow…
Activity diagrams represent Use
  What about Definition? The bubbles on act’s are Actions, not Activities!
Activity models are usually built without regard to functional hierarchy
  Tools don’t support functional hierarchy very well.
Recommendation:
  Don’t put an Action on an activity diagram without having it call an Activity. Use only CallBehaviorActions.
  Manage the Activities in a separate set of packages, just like blocks.
  Generate functional hierarchies using bdd’s

## Slide 10: Activity Model & Functional Hierarchy

## Slide 11: Issue #4: Containment vs. Composition
This is a common issue for even experienced modelers
Containment relation is seldom seen on diagrams (crosshair), but is the basis for the model browser.
  Packages exist as “containers” for organizing the model
  Blocks, Requirements can also be “containers”… but I advise against it!
Composition (black diamond) is a way of representing Use on a Definition diagram.
  Composition role names on the bdd correspond to part/action names on the ibd/act.

## Slide 12: Containment in Browser & Package Diagram

## Slide 13: Containment/Package Structure Suggestions
Structural hierarchy:
  Treat every block as reusable
    Put them in a package where modelers can find them… based on what they are, not how they are used
  Build ibd’s from blocks in the browser (drag & drop). Autorender the bdd’s after the ibd’s have been built.
    Untyped parts are poor modeling form
Functional hierarchy
  Treat every activity as reusable
  Build act’s from activities in the browser. Most tools won’t autorender bdd’s, so this will be a little more work.
Data/Info Model
  Enforce all data types in one convenient containment hierarchy
  Put FlowSpecifications or InterfaceBlocks in the hierarchy too

## Slide 14: Package Diagram Organizing the Model
By Diagram/Model Type
By Abstraction Level
By IPT
pkg
SampleModel
[
by diagram type
]
Behavior
Structure
Requirements
Use Cases
pkg
SampleModel
[
by level
]
Enterprise
System
Logical Design
Physical
Design
EngrAnalysis
Verification
pkg
SampleModel
[
by IPT
]
Architecture
Team
Requirements
Team
IPT A
IPT B
IPT C

## Slide 15: Issue #5: SysML vs. Matlab (Descriptive vs. Analytical Models)
SysML models are descriptive
Performance models (like Matlab) are analytical

## Slide 16: Descriptive Models & Analysis Models
Descriptive/Specification Model
view-
point
External Requirements
traceability,
rationale
analysis
needs
closed form
discrete event
network
Analysis Models & Simulations
System Documentation & Specifications
per-
formance estimates
Model Based Engineering Discipline
Arrows indicate interactions that could potentially be automated
Linkage to Other Disciplines/IPTs

## Slide 17: Parametric Modeling Links Descriptive & Analytical Models
Systems engineers tend not to build parametric models
  Powerful, unique capability to check model consistency and integrity
  Linkage to external analysis capabilities/simulations/models
  Test and validation implications
This is changing with better vendor support
  Phoenix ModelCenter “MBSE Pak” plugin
  InterCAX plugin for MagicDraw and Rhapsody
When this capability works, it is more impressive, meaningful, and powerful than animating the SysML model!

## Slide 18: Parametric Example: Air Compressor – Definition & Use
Figure 3.11
Figure 3.12
Copyright © 2012, Elsevier Inc. All rights Reserved.

## Slide 19: Issue #6: Values, Value Types, Units and Dimensions
We don’t think about adding specific values until the performance analysis has already started.
  Once we start adding values, we discover that we need units and dimensions too. This adds considerable work for the modeler.
Default values can be added to the block, but actual values require instance specifications
  Modelers tend to have initial difficulty with instances. Most tools don’t support this well
Standard units and dimensions can be imported as library
  But custom units and dimensions are almost always required for a new domain
  ValueTypes must be built from the Units and Dimensions before they can be used. Not a big job, but often overlooked.
“A model without values has no value” – Dr. Darren Kelly

## Slide 20: Issue #7: Modeling Functionality vs. Model Execution
Model execution is becoming important for checking dynamic consistency of the system design.
“SysML doesn’t execute”
  It was never intended to! Nor does it calculate.
  Some tools provide execution capability, if you follow their modeling rules (Rhapsody, MagicDraw Cameo, etc.)
SysML is compatible with foundational UML (fUML) and its action language (ALF)
The burden of model execution: In addition to a semantically correct behavioral model, there needs to be:
  A simulation environment, including keeping track of model time
  A stimulus or input file
  A visualization/animation capability
  Resource constraint/utilization based on allocation to structure
Some of the value of model execution may be gained using linked external models, e.g. Extend
System model execution is not a substitute for MS&A.
Choose, but choose wisely!

## Slide 21: Backup

## Slide 22: 4 Pillars of SysML – ABS Example
definition
use
1. Structure
2. Behavior
3. Requirements
4. Parametrics
interaction
state
machine
activity/
function
Notes: Structure
  e.g., system hierarchies, interconnections
Behavior
  e.g., function-based behaviors, state-based behaviors
Properties
  e.g., parametric models, time variable attributes
Requirements
  e.g., requirements hierarchies, traceability

## Slide 23: Cross Connecting Model Elements in ABS example
1. Structure
2. Behavior
3. Requirements
4. Parametrics
allocate
satisfy
value binding
Verify
(via interaction)
Notes: 4 types of cross-connecting principles:
Allocation
Requirement satisfaction/derivation
Value Binding/Parametrics
Requirement Verification

## Slide 24: “SysML Light” (Basic Capability)
© 2012 Elsevier Inc, “A Practical Guide to SysML”
req [Package] Requirements
bdd [Package] Structure
par [Block] Analysis

## Slide 25: Related Activities – Georgia Tech
Copyright Georgia Tech - slide used by permission

## Slide 26: Three Ways to Model Behavior: Each Invokes Activities
Activity
+effect
Action 1
Action 2
Activity X1
State X
Activity Y1
Activity Y2
State Y
Transition Activity T1
Op 2.1
Class 2
Op 2.1 (msg:type)
method
entry
exit
doActivity
invocation
Class1
Class 1
State Machine Model
Activity Model
Interaction Model
(sequence
diagram)