## Slide 1
1.1.6
INCOSE/OMG MBSE Initiative
PBSE Patterns Challenge Team
Meeting: September 2, 2014
Team web site: http://www.omgwiki.org/MBSE/doku.php?id=mbse:patterns:patterns

## Slide 2
2
(Schedule adjustable as needed)

## Slide 3
Primary objective of today’s meeting:
  Review next segments of the team’s project patterns
This Challenge Team is concerned with configurable, re-usable system models, called “S*Patterns”:
  Models containing a certain minimal set of elements are called S*Models
  May be expressed in any modeling language (e.g., SysML, or other)
  Re-usable, configurable S*Models are called S*Patterns
  By “Pattern-Based Systems Engineering” (PBSE) we mean MBSE enhanced by these generalized assets
  These are system-level patterns (models of whole managed platforms), not smaller-scale component design patterns
These are the team’s pattern projects known to be underway:
  Multi-domain product/manufacturing process example (Oil Filter Family) (Bill Schindel, Stephen Lewis, Saumy Sanyal, David Cook)
  Mil/Aero Electronic Systems (Tamara Valinoto)
  RC / Autonomous Car (Troy Peterson)
  Verification Systems (Andy Pickard)
3

## Slide 4: Walk-through of some initial S*Pattern segments
Stakeholders, stakeholder Features, and their Associations:
  Stakeholders: People or Organizations with a “stake” in the behavior of the system of interest.
  Features: Selectable sets of stakeholder-valued system behaviors, in (often non-technical, subjective) language and concepts of stakeholders.
  Feature Attributes: Parameterize the Features, with variables that the stakeholder cares about (e.g., Passenger Seating Capacity for a bus)
Once we establish a Pattern for a Platform or Product Line System, specific configurations are generated by selection (population) of Features, and setting values for Feature Attributes.

## Slide 5: An example S*Pattern Extract
Lubricant (Oil) Filter Product Family

## Slide 6: Example S*Pattern Stakeholder Feature Overview Model
6

## Slide 7: Example S*Pattern Stakeholder Feature Model Extract
Feature | Feature Attribute | Multi-Instance | Attribute Definition | Attribute Units | Attribute Values
Optimal Product Configuration Feature | Product Configuration | X | Identifies the configuration of the product, as a model ID. Multiple configurations may be populated. | N/A | 
Optimal Product Configuration Feature | Product Configuration Volume |  | The number of units of this product configuration produced per year. | Units/Year | 
Filter Application | Application Type | X | The type of lubricated system application supported by a lubricant filtration system. More than one type may be instantiated for a single product configuration. | N/A | Consumer Automotive, Commercial Automotive, Fixed Base Engine System, Harsh Environment, High Temperature Environment, Cold Environment
Filter Application | Application Volume |  | The number of units of this application placed into service during a year. | Units/Year | 
Filter Application | Lubricant Type |  | The type of lubricating fluid to be used. | N/A | 
Filter Application | Lubricant Flow Rate |  | The rate at which the lubricating fluid must be circulated in order to meet equipment lubrication objectives. | GPM | High, Medium, Low
Filter Application | Lubricant Pressure Range |  | The amount of hydraulic pressure under which the lubricant will circulate. | PSI | High, Medium, Low
Filter Application | Filter Efficiency Class |  | The profile of filtration efficiency provided by the filter | N/A | 
Mechanical Compatibility Feature | Spatial Form Factor |  | The class of three dimensional structure of a component, subsystem, or space within a system reserved for a component or subsystem. | N/A | 
Mechanical Compatibility Feature | Mechanical Interface Type |  | The mechanical class of the interface between the oil filter and the equipment to which it is connected. | N/A | 
Cost of Operation Feature | Lubricant Life |  | The amount of time that a lubricant is intended to operate, meeting requirements within the specified environment, before it is replaced. | Hours | 
7

## Slide 8: Example S*Pattern Stakeholder Feature Overview Model
8

## Slide 9: What modeling tools, languages will we use?
S*Metamodel is modeling language independent:
  Readily expressed in SysML or other modeling languages.
  For INCOSE work, if the sub-team does not have a conflicting goal, we’d encourage use of SysML, familiar to more in INCOSE.
  Be prepared to learn a few things that the modeling language standards have not quite caught up with yet.
  One of our team’s spin-offs is feedback to Sandy Friedenthal’s inputs on future SysML releases.
  If you have a different language in mind, we’ll help.
9

## Slide 10: Examples from Enterprise Architect (a SysML Modeling Tool)
10

## Slide 11: Examples from Enterprise Architect (SysML Modeling Tool)
11

## Slide 12: Discussion of your Patterns . . .
Stakeholders, Features
12

## Slide 13: External “domain model” for System of Interest
Will later help us identify all the external interactions with System of Interest.
  So what? All system black box requirements are identified with (may be discovered through) those interactions.
Domain diagram shows Actors, Interfaces, Input-Outputs or Relationship--:
  Actors: People or other Systems that directly interact with the system of interest, by exchanges of force, energy, mass, or information.
  Input-Outputs: The exchanged forces, energy, mass, or information.
  Domain Architecture Relationships: Alternative way to summarize input-outputs
  Interfaces: Associations of Systems (that “have” the interfaces), Input-Outputs (that “pass through” the interfaces), Interactions (that “describe behavior” at interfaces, and Systems of Access (that provide the external media of interaction).
13

## Slide 14: Domain model for Oil Filter System
14

## Slide 15: Extract from equivalent SysML Domain Model, in EA Tool
15

## Slide 16: Domain model for Manufacturing System (of Oil Filter)
16

## Slide 17
Challenge Team goal for second half of 2014:
  Make enough sub-team progress on selected patterns important to members to support . . .
  One or more related INCOSE IS2015 papers for Seattle (paper drafts due Nov 2014, complete in Mar 2015—two currently known in progress)
  One or more related INCOSE GLRC2014 presentations for Chicago (October, 2014—one currently known accepted)
In support of this goal:
  Bill Schindel is holding bi-weekly, web-based pattern review sub-team work sessions (e.g., 90 minutes) throughout the second half of 2014
  Typically meet every other Monday, 4:00 – 5:30 PM EST (like today’s)
  Purpose of these sessions to assist sub-teams in preparing S*Patterns conforming to S*Metamodel and meeting each team’s application goals.
17
Sessions | Configurable S*Pattern Construction
Aug | Configurable Features Model; Domain Model
Sep | Domain Model; Interactions; States
Oct | Detail Interactions; Requirements; Attribute Couplings
Nov | Logical Architecture; Detail Interactions; Requirements
Dec | Physical Architecture; Failure Modes
Jan | More about configuration rules

## Slide 18: Scheduling and communications
Currently planned next meeting dates:
  Monday, Sept 15, 4:00 – 5:30 PM EST
  Monday, Sep 30, 4:00 – 5:30 PM EST
  And every other Monday thereafter . . .
Team web site:
http://www.omgwiki.org/MBSE/doku.php?id=mbse:patterns:patterns
18

## Slide 19: Related Activities by Other WGs and MBSE Initiative
Working with Rick Dove (Agile Systems WG, Security WG) on an IW2015 MBSE Workshop break-out session:
  On Agile Systems, System Patterns, and Composable Designs
We’d like to have cooperative activities with other WGs:
  e.g., Biomedical / Healthcare
Other groups in the MBSE Initiative are creating a cloud resource for working groups and teams such as ours:
  On-line shared models repository, for sharing models
  On-line access to limited set of tool vendor licenses, for use in INCOSE projects
News from other members, WGs:
To whom else should we be reaching out?
19

## Slide 20: Back up materials—from earlier meetings of this Challenge Team

## Slide 21
Patterns Demand Strongest Underlying Models
The S*Metamodel describes the smallest set of ideas necessary to model a system for purposes of engineering or science:
  Most of them familiar to modelers, and all of them basic to the training of engineers and scientists—but not always found in their system models.
  A metamodel is a model of other models;
  Sets forth underlying concepts of Requirements, Designs, Failures, Trade-offs, etc. (not modeling language syntax)
Simple summary of detailed S* Metamodel.
The resulting S*Models may be expressed in SysML or other modeling languages, and constructed / reside in numerous commercial tools and information systems.
Has been applied to SE in aerospace, transportation, medical, advanced manufacturing, communication, construction, consumer, other domains.
21

## Slide 22
  The PBSE approach respects the systems engineering tradition, body of knowledge, and historical lessons, while providing a high-gain path forward.
  An S* Pattern is a configurable, re-usable S* Model. It is an extension of the idea of a Platform (which is a configurable, re-usable design). The Pattern includes not only the Platform, but all the extended system information (e.g., requirements, risk analysis, design trade-offs & alternatives, decision processes, etc.):
  By including the appropriate S* Metamodel concepts, these can readily be managed in (SysML or other) preferred modeling languages and tools—the ideas involved here are not specific to a modeling language or specific tool—ported to several.
  The order-of-magnitude changes have been realized because projects that use PBSE rapidly start from an existing Pattern, gaining the advantages of its content, and feed the pattern with what they learn, for future users.
  The “game changer” here is the shift from “learning to model” to “learning our (your) model”, freeing many people to rapidly configure, specialize, and apply patterns to deliver value in their model-based projects.
22

## Slide 23: A little more about S*Patterns
Fixed (Pattern) Portion, Variable (Configuration) Portion, and the Configuration Process:
  The generalized S*Pattern is expressed in exactly the same S*Metamodel classes and relationships as a specific configured S*Model derived from it.
  “Configuring” a pattern means a process limited to exactly two things:
    Populating (or de-populating) instances of classes and relationships
    Setting the values of attributes (parameters)
23

## Slide 24: A little more about S*Patterns
Having an S*Pattern meeting the underlying S*Metamodel demands has some surprising positive consequences beyond basic benefits of MBSE:
  The Stakeholder Feature portion of the pattern directly generates a formal Trade Space / Scoreboard for arguing, defending all decisions.
  “Configuring” the (low dimension) Stakeholder Feature portion of the Pattern for a specific project or system configuration can “automatically” generate the (high dimension) configured Technical Requirements for that system configuration.
  For a sufficiently built-out S*Pattern, the same applies to the System Design (physical architecture, allocations, attribute couplings, etc.).
  The S*Pattern can rapidly generate very complete first draft FMEA tables, since S*Features lead directly to modeled Effects, S*Requirements lead directly to modeled Counter-Requirements (functional failures), S*Design Components lead directly to modeled Failure Modes, and combinatorial FMEA analyses of the three together may be rapidly generated by machine matching algorithm.
All these produce much faster initial drafts that are much more complete and consistent than manual approaches, but which can (should) still be subject to the normal human SME review and update:
  We are not suggesting turning our thinking and fate over to the model, without human judgment, expertise, etc.
24

## Slide 25: Example S*Pattern Application Domain Model
25

## Slide 26: Example S*Pattern Manufacturing Domain Model
26

## Slide 27: Example S*Pattern State (Modes) Model
27

## Slide 28: Example S*Pattern Interaction Overview Model
28

## Slide 29: Example S*Pattern Feature-Interaction Associations Model (Part of Pattern Configuration Model)
29

## Slide 30: Example S*Pattern Interaction Overview Model Extract
Interaction Name | Interaction Definition | Oil Filter System | Service Person | Mounting System | Ambient Air | Removed Solid Contaminant | Lubricant In Filtration | Removed Water | Local Surface | Lubricated System | Lubricant In Distribution | Lubricant Distribution Pump | Lubricant Transport Containment | Waste Management System | Manufacturing System | Distribution System | Package | Buyer
Filter Lubricant | The interaction during which the oil filter system filters the lubricant in filtration. | X |  | X |  | X | X | X |  | X | X | X | X |  |  |  |  | 
Impregnate Lubricant Additive | The interaction during which the manufacturing system impregnates the oil filter with lubricant additive. | X |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  | 
Fold Accordion Pleats | The interaction during which the manufacturing system folds the sheet oil filter element into the form of accordion pleats. | X |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  | 
Cut & Separate Filter Element | The interaction during which the manufacturing system cuts and separates individual oil filter elements. | X |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  | 
Wind Filter Element | The interaction during which the manufacturing system winds the fiber oil filter element into a cylindrical shape. | X |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  | 
Insert Filter Element | The interaction during which the manufacturing system inserts the filter element into the filter housing. | X |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  | 
Perform End Seal Bonding | The interaction during which the manufacturing system bonds the end seal of the oil filter. | X |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  | 
Inspect Product | The interaction during which the manufacturing system inspects the finished oil filter product. | X |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  | 
Insert Into Package | The interaction during which the manufacturing system inserts the finished oil filter product into the package. | X |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X | 
Remove Filter Media | The interaction during which maintainer removes the filter media from the oil filter system. | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Clean Filter Media | The interaction during which the maintainer cleans the filter media. | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Insert Filter Media | The interaction during which the maintainer inserts the filter media back into the filter housing. | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Roll Filter Element | The interaction during which the manufacturing system rolls the sheet filter element into a cylindrical shape. | X |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  | 
Transmit Shock & Vibration | The interaction during which the oil filter system is subject to, and transmits, mechanical shock and vibration originating externally. | X |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Monitor Filter | The interaction through which the service person or lubricated equipment monitors the condition of the oil filter. | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Prevent Vapor Leakage | The interaction through which the oil filter prevents undue quantities of gaseous vapor contaminants from reaching the external local atmosphere. | X |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  | 
Prevent Lubricant Leakage | The interaction through which the oil filter prevents undue quantities of lubricant from escape from its portion of the lubrication loop. | X |  |  |  |  | X |  | X |  |  |  |  |  |  |  |  | 
Transmit Thermal Energy | The interaction through which the oil filter receives and transmits thermal energy, originating in external components. | X |  | X | X |  | X |  |  |  |  |  |  |  |  |  |  | 
30

## Slide 31: Example S*Pattern Logical Architecture Model
31

## Slide 32: Example S*Pattern Requirements Model -- Extract
Interaction | Role | ID | Requirement Statement
Filter Lubricant | Oil Filter System | OF-50 | For a Return Lubricant stream of [Lubricant Viscosity Range] and [Lubricant Pressure Range], the Oil Filter shall separate Filtered Contaminant particles from the Lubricant output stream, according to the [Filter Particle Size Distribution Profile].
Filter Lubricant | Oil Filter System | OF-51 | The Oil Filter shall operate at lubricant pressure of [Max Lubricant Pressure] with structural failure rates less than [Max Structural Failure Rate] over an in-service life of [Min Service Life].
Filter Lubricant | Oil Filter System | OF-52 | The Oil Filter shall accommodate a Lubricant flow rate of [Lubricant Flow Rate].
Filter Lubricant | Lubricant Distribution Pump | OF-53 | The Pump shall maintain oil pressure within the [Lubricant Pressure Range].
Filter Lubricant | Lubricant In Filtration | OF-54 | The Lubricant in Filtration shall have viscosity within the [Lubricant Viscosity Range].
Filter Lubricant | Lubricated Machine | OF-55 | The Lubricated Machine shall contribute a Contaminant Load to the lubricant, not to exceed [Lubricant Contaminant Load Rate].
Filter Lubricant | Lubricated Machine | OF-56 | The Lubricated Machine shall not heat the lubricant above [Max Lubricant Temperature].
Inject Additive | Oil Filter System | OF-57 | The Oil Filter shall inject additive of type [Additive Type] into the Lubricant flow, at a rate of [Additive Injection Rate] per unit of lubricant flow, over the service life of the filter element.
Remove Filter Media | Oil Filter System | OF-90 | The Oil Filter System shall permit the removal of its used Filter Media.
Remove Filter Media | Oil Filter System | OF-91 | The Oil Filter System filter media removal process shall allow the service person to avoid direct contact contamination with filtered contaminants and lubricant.
Clean Filter Media | Oil Filter System | OF-92 | The Oil Filter System shall permit the cleaning of its used Filter Media, for reuse purposes, using cleaning solvent and method of type [Filter Media Cleaning Method and Solvent].
Clean Filter Media | Oil Filter System | OF-93 | The Oil Filter System filter cleaning process shall allow the service person to avoid direct contact contamination with filtered contaminants and lubricant.
Insert Filter Media | Oil Filter System | OF-94 | The Oil Filter System shall permit the insertion of its Filter Media, of type [Filter Media Type].
Insert Filter Media | Oil Filter System | OF-95 | The Oil Filter System filter media insertion process shall allow the service person to avoid direct contact contamination with filtered contaminants and lubricant.
Transmit Shock & Vibration | Oil Filter System | OF-100 | The system shall meet its other requirements when subject to a vibration spectrum not exceeding [Max Vibration Spectrum] during its in-service life.
Transmit Shock & Vibration | Oil Filter System | OF-101 | The system shall meet its other requirements when subject to shock intensity and frequency not exceeding [Max Shock Intensity and Frequency] during its in-service life.
Monitor Filter | Oil Filter System | OF-102 | The system shall provide a means of inspection of its remaining service life before requiring servicing, using [Filter Monitoring Method].
Prevent Vapor Leakage | Oil Filter System | OF-103 | When operating within its rated lubricant pressure and temperature, at altitudes not exceeding [Max Service Altitude], the system shall maintain Vapor Leakage to the ambient air space below [Max Vapor Leakage Rate].
Prevent Lubricant Leakage | Oil Filter System | OF-104 | When operating within its rated lubricant pressure and temperature, at altitudes not exceeding [Max Service Altitude], the system shall maintain Fluid Leakage to the surrounding space below [Max Fluid Leakage Rate].
Transmit Thermal Energy | Oil Filter System | OF-105 | The system shall meet its other requirements while operating in external ambient air temperatures of [External Temperature Range] and lubricant temperatures of [Lubricant Temperature Range].
Install Filter | Oil Filter System | OF-106 | The Oil Filter shall be manually installable in ten minutes or less, using only a screwdriver.
Install Filter | Oil Filter System | OF-107 | The Oil Filter shall have installation instructions printed on its exterior surface, in [National Language] language.
Install Filter | Oil Filter System | OF-110 | The Oil Filter shall not present sharp edge hazards to the installer during the installation process.
Install Filter | Oil Filter System | OF-111 | The Oil Filter shall be clearly labeled with instructions to shut down pressurized equipment prior to installation.
Install Filter | Service Person | OF-112 | The Service Person with the visual acuity and hand strength of an average 40 year old adult shall be able to install the Oil Filter System.
Install Filter | Service Person | OF-113 | The Service Person shall be capable of reading [National Language] at the tenth grade level.
32

## Slide 33: Pattern-Based Systems Engineering (PBSE)
Pattern-Based Systems Engineering (PBSE) has two overall processes:
  Pattern Management Process: Generates the general pattern, and periodically updates it based on application project discovery and learning;
  Pattern Configuration Process: Configures the pattern into a specific model for application in a project.
33

## Slide 34: Why do most representations of the systems engineering process appear to assume starting from no formal knowledge about the system of interest & its domain?
34
Business process optimized for PBSE fulfill a different vision:

## Slide 35: Pattern Configurations
Product/Feature | Ice Road Trucking | Consumer Auto | Commercial Auto | Fixed Based Engine
Engine Lubricant Filtration Feature | Cold Environment | Consumer Automotive | Commercial Automotive | Fixed Based Engine System
Mechanical Compatibility Feature | X | X | X | X
Cost of Operation Feature | X | X | X | X
Reliability Feature | X | X | X | X
Maintainability Feature | X | X | X | X
Additive Feature | No. 7 Efficiency Boost | No. 5 Life Extension | No. 6 Efficiency Boost | No. 3 Efficiency Boost
Environmentally Friendly Feature | X | X | X | X

## Slide 36: Pattern Configurations, Model Compression
A table of configurations illustrates how patterns facilitate compression;
Each column in the table is a compressed system representation with respect to (“modulo”) the pattern;
The compression is typically very large;
The compression ratio tells us how much of the pattern is variable and how much fixed, across the family of potential configurations.
36

## Slide 37
Eric Berg, “Affordable Systems Engineering: An Application of Model-Based System Patterns To Consumer Packaged Goods Products, Manufacturing, and Distribution”, at INCOSE IW2014 MBSE Workshop, 2014.
Bill Schindel, Troy Peterson, “Introduction to Pattern-Based Systems Engineering (PBSE): Leveraging MBSE Techniques”, in Proc. of INCOSE 2013 Great Lakes Regional Conference on Systems Engineering, Tutorial, October, 2013.
W. Schindel, “System Interactions: Making The Heart of Systems More Visible”, in Proc. of INCOSE Great Lakes 2013 Regional Conference on Systems Engineering, October, 2013.
Bill Schindel, Troy Peterson, “Introduction to Pattern-Based Systems Engineering (PBSE): Leveraging MBSE Techniques”, in Proc. of INCOSE 2013 International Symposium, Tutorial, June, 2013.
”Abbreviated Systematica Glossary, Ordered by Concept, V 4.2.2, ICTT System Sciences, 2013.
W. Schindel, “Introduction to Pattern-Based Systems Engineering (PBSE)”, INCOSE Finger Lakes Chapter Webinar, April 26, 2012.
------------------, “Integrating Materials, Process & Product Portfolios: Lessons from Pattern-Based Systems Engineering”, in Proc. of 2012 Conference of Society for the Advancement of Material and Process Engineering, 2012.
------------------, “What Is the Smallest Model of a System?”, in Proc. of the INCOSE 2011 International Symposium, International Council on Systems Engineering (2011).
------------------, “The Impact of ‘Dark Patterns’ On Uncertainty: Enhancing Adaptability In The Systems World”, in Proc. of INCOSE Great Lakes 2011 Regional Conference on Systems Engineering, Dearborn, MI, 2011
------------------l, “Failure Analysis: Insights from Model-Based Systems Engineering”, in Proceedings of INCOSE 2010 Symposium, July 2010.
J. Bradley, M. Hughes, and W. Schindel, “Optimizing Delivery of Global Pharmaceutical Packaging Solutions, Using Systems Engineering Patterns”, in Proc. of the INCOSE 2010 International Symposium (2010).
W. Schindel, “Pattern-Based Systems Engineering: An Extension of Model-Based SE”, INCOSE IS2005 Tutorial TIES 4, (2005).
------------------, “Requirements Statements Are Transfer Functions: An Insight from Model-Based Systems Engineering”, in Proc. of INCOSE 2005 International Symposium, (2005).
W. Schindel, and V. Smith, “Results of Applying a Families-of-Systems Approach to Systems Engineering of Product Line Families”, SAE International, Technical Report 2002-01-3086 (2002)..
37

## Slide 38
https://sites.google.com/site/incosepbsewgtempaccess/
The references above may be downloaded from: